# INPUTS CHECKLIST COMMERCIAL

# Tienda cabezas matapuncho

# tarifa comercial codigo 365n# medidor 162206 (Foto 387, )

La tienda del Sr. Marcos Cabezas Matapuncho esta rodeado de pocos edificios. La entrada principal esta al Norte ( Foto 391).se encuentra en la calle española frente al Parque de Marta Roldós.

La altura referente a las edificaciones que le rodean es variable, la tienda tiene forma rectangular.

En la Fachada uno podemos encontrar dos puerta , la tienda ocupa  la puerta a mano derecha donde se ingresa a la tienda y a mano izquierda podemos observar la vitrina congelador (foto 377) y a mano izquierda stans con la alimentos de primera necesidad ( Foto 386) y encontramos la ventana de madera sin vidrio donde entra aire fresco y da sombra., en la parte de atrás de la tienda encontramos una puerta abierta donde  entra aire y luz.

El techo de afuera es de ternil, y se ve viejo, aquí no se podría instalar paneles solares, ya que el techo no se en buen estado. ( Foto 373).

La estructura de la tienda es de pilares de madera de Matasarna, mas cemento.

El Interior de la tienda, mirando hacia el techo puedes observar un techo visto donde encuentras las fijas de matasarno y se ve el techo de ternil, aquí están ubicados los focos ahorradores, y lámparas floresentes con conexiones  en mal estado (Foto 380, 381,390).

Cuando entras por la segunda puerta puedes observar la instalación de la vitrina congelador y tiene un alambre con citan adhesiva ( Foto 376,) y una toma corriente sin tapa( Foto 378)

Tienen una radio, una televisión, una vitrina congeladora, y una refrigeradora que no  usan.

Encontré 2 medidores, el cual uno es el que esta en la lista de Elegalapagos (Foto 387), y el otro no esta en la lista ( foto 374) y  se ocupan para la tienda.

Nota:	 Esta tienda Necesita cambiar completa mente sus alambres de techo y tener mejores conexiones para los aparatos eléctricos.El piso de la tienda es de cemento.

A. Building configuration

| Construction year | 1993 |
| --- | --- |
| Orientation of main entrance | Norte |

Density of nearby obstructions

| ( Very dense | ( Moderately dense | X Few buildings | ( Free standing |
| --- | --- | --- | --- |

Height of surrounding buildings:

| ( Higher | ( Same | ( Shorter | X Variable |
| --- | --- | --- | --- |

Building’s Shape:

| ( Square | X Rectangular | ( Square with Atrium |
| --- | --- | --- |

External Walls colour 		( dark		X medium	( light

Roof colour 			X dark		( medium	( light

| Yearly Energy consumption 01 del 2002 al 07 del 2003 |
| --- |
| Electricity (kWh) Annual bill: | 1996kw $177.42 |

Annual operation:	from month  1    to month   12

Heating period:		from month      to month         .

Cooling period:		from month      to month      .

# B. Description of envelope construction

# B1.    Facade

Attention: All shading percentages below are related to total window area.

|  | Facade 1 | Facade 2 | Facade 3 | Facade 4 |
| --- | --- | --- | --- | --- |
| Facade orientation | Norte | Oeste | Sur | Este |
| Facade Area (m²) | 18 | 15 | 18 | 15 |
| Walls U-value [W/(m²K)] | cemento | con vigas | de | madera |
| Windows area, % of facade area | 1/6% | 0 | 0 | 0 |
| Percentage of natural shading (%) | 0 | 0 | 0 | 0 |
| Percentage of external vertical blinds (%) | 0 | 0 | 0 | 0 |
| Percentage of external louvers (%) | 0 | 0 | 0 | 0 |
| Percentage of overhangs (%) | 0 | 0 | 0 | 0 |
| Percentage of awnings (%) | 0 | 0 | 0 | 0 |
| Percentage of side fins (%) | 0 | 0 | 0 | 0 |
| Percentage of shutters (%) | 0 | 0 | 0 | 0 |
| Percentage of internal vertical blinds (%) | 0 | 0 | 0 | 0 |
| Percentage of internal louvers (%) | 0 | 0 | 0 | 0 |

# B2.    Floor

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Floor area on the ground | 47 | cemento |
| Floor over non-heated zone | 0 |  |
| Floor exposed to the exterior (pilotis) | 0 |  |

# B3.    Roof

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Exposed roof area | 97 | Deternil, con fijas de Madera de matasarno |
| Roof area to non heated spaces | 0 |  |
| Roof glazed area | 0 |  |

#### C.    General inputs

| Parameter | Value | Description |
| --- | --- | --- |
| Site area, m² | 47 | Total lot area |
| Area of foundations, m² | 47 | Area of typical floor |
| Green Areas, m² | 0 | Green Areas |
| Height of typical floor, m | 2.70 | Height of typical floor |
| Number of floors | 1 | Number of floors, ground floor included. |
| Number of basement floors | 0 | Number of floors, below ground floor. |
| Number of rooms | 2 | Number of rooms |
| Number of staircases | 0 | Number of internal staircases |
| Gross floor area, m² | 47 | Gross floor area (basement included) |
| Garage area, m² | 0 | Garage area in basement |
| Heated floor area, m² | 0 | Heated floor area |
| Conditioned area, m² | 0 | Conditioned area |
| Supply air flow rate in rooms, m3/h | 0 | Supply air flow in rooms |
| Installed heating power, kW (Thermal) | 0 | Installed heating power |

#### D.   Inputs for heating / cooling

| Heating set point, °C | 0 | The internal temperature is the set point temperature during the heating season. |
| --- | --- | --- |
| Cooling set point, °C | 0 | The internal temperature is the set point temperature during the cooling season. |
| Temperature control | 0 | 1: Bad control (No thermostatic control and no night set back, regulary overheating during winter) 2. No control (No thermostatic control and no night set back) 3. Standard (Thermostatic control of the indoor temperature during the heating season OR night set back of 3 °C) 4. Good control (Thermostatic control AND night setback of up to 3 °C during the heating season) 5. Advanced control (Probabilistic control of the heating system based on an estimated weather forecasts and adapted user behaviour) |
| Infiltration, ach | 0 | 1. 0.1ach 2. 0.5 ach 3. 1 ach 4. 1.5 ach |
| Boiler efficiency, % | 0 | 1. Low efficiency (Boiler in poor stage. Insulation of boiler and storage is missing. Boiler room and pipes in the boiler room are not insulated) 2. Under medium efficiency (Boiler is more than 15 years old or in a poor condition of maintenance. Insulation level of boiler and storage is insufficient) 3. Medium (Boiler is less than 15 years old OR in perfect condition. Insulation level of boiler and storage is sufficient.) 4. Over medium efficiency (Boiler is less than 15 years old and in perfect condition. Insulation level of boiler and storage is sufficient.) |
| Number of existing ceiling fans | 0 | Number of existing ceiling fans |

#### E.  Inputs for hot water production

| Fuel for domestic hot water production | 0 | 1: oil, 2:gas, 3: electricity |
| --- | --- | --- |
| Solar collectors surface, m2 |  |  |
| Available space for additional solar collectors, m2 | NO | Esta en mal estado el techo es viejo |

Available space towards south, for solar collectors:

| ( | X | ( |  |
| --- | --- | --- | --- |

#### Inputs for artificial lighting

|  | Internal type | External type | Power (Watt) | Daily use (h) | Remark |
| --- | --- | --- | --- | --- | --- |
| Type of existing lamps 1: standard incandescent, 2: efficient incandescent, 3: tube fluorescent, 4: compact fluorescent, 5: discharge, 6:otherFocos ahorradores | Tipo/N#/KW 1/2/100 3/1/20 3/1/40 6/2/20 |  | 100 20 40 20 | 4 Horas |  |

Inputs for electric CONSUMPTION

LOCALITY :Calle Española frente al Parque de Marta Roldos

N. OF PERSON:1

| Contract typology: Residential Commercial Industrial Other | Type of fee: 14.68 |
| --- | --- |
| Power (kW) Voltage (V): 110 Frequency (Hz): 60 Safety equipments: | Consumption (kWh/year) |

| Person | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21/22 | 22/23 | 23/24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Plants-Equipments Hours | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21-22 | 22-23 | 23-24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lighting (W) |  |  |  |  |  |  |  |  |  |  |  |  | x | xx | xx | xx |  |  |  |
| Fan (W) |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Food Refrigerator (W) |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Hot Water (W) |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Cooling (W) |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

HOUSEHOLD APPLIANCE

|  | Number | Power (Watt) | Total Daily use(h) | Hour of use | Remark |
| --- | --- | --- | --- | --- | --- |
| Radio/ Television | 1 1 | 80kw | 2 1 | 2 1 |  |
| Computer | 0 | 0 | 0 | 0 |  |
| Domestic refrigerator Vitrina Congelador | 1 1 | 0 12amp | 0 24 Horas | 0 24 horas | No utiliza Guarda alimentos |
| Freezer | 1 | 120kw | 24 horas | 24 | Una semana la prende y otra no |
| Ceiling fan | 0 | 0 | 0 | 0 |  |
| Washing machine | 0 | 0 | 0 | 0 |  |
| Electrical space heating | 0 | 0 | 0 | 0 |  |
| Electrical DHW | 0 | 0 | 0 | 0 |  |
| Other (cafeteras, sambuchera) | 0 | 0 | 0 | 0 |  |
| Kitchen : Cooking set Oven | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 |  |
| AC system 1) Split system 2) HVAC | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 |  |