# INPUTS CHECKLIST COMMERCIAL

# Mini Market 2000

# tarifa comercial codigo 824 n# medidor 54798448 (Foto 615)

El Mini Marka 2000 se encuentra ubicado en la Av. charles Darwin, y Av.Hernán Malville, es la calle principal y es un sector muy transitado por automóviles y gente. Es moderately dense con respecto a las edificaciones, es una de las edificaciones mas altas dentro de el grupo de construcciones que le rodea.

El mini market 2000 tiene forma de rombo (Foto 621). La entrada principal esta al Este , la fachada uno podemos encontrar una puerta de vidrio transparente , con aluminio ( Foto 639), al ingresar encontramos todos los productos de primera necesidad bien organizados, y es un lugar fresco (Foto 623), podemos observar a la entrada a mano izquierda un congelador que tiene 5 años de marca Kelvinator( Foto 610, 611) y a mano  derecha dos cámaras de ambiente donde mantiene fría las bebidas, estos equipos lo tienen 5 años (Foto 609), mirando hacia frente encontramos una cámara de frió que fue hecha aquí y tiene 3 años( Foto 608), al fondo podemos observar otro congelado que tiene 7 años ( foto 607). Todos estos equipos no tienen placas para poder distinguir las características.

Podemos observar que tienen un piso de baldosa , mantiene fresco el lugar ( foto 625); podemos encontrar 5 lámparas florecentes y una dañada en el interior de la tienda, el techo es de cemento (foto 632, 633).

En la Fachada uno  encontramos 4 ventanas de  (Foto 626,614), de vidrio trasparente y aluminio.

También podemos encontrar un toldo de cing de 13.65 metros de largo (Foto 621),  se encuentra  en el exterior, es  de color azul con blanco, este protege del sol, y da sombra.

En la fachada dos hay 6 vidrios transparentes con aluminio (Foto 617), y tiene el techo que sobre sale de cemento y este da sombra a la fachada (Foto 613).

En La fachada uno y dos encontramos 5 puertas lanfor, están son de protección para que nadie entre, (foto 628).

El piso del exterior es hecho de cemento con piedra y decoración de Baldosa (Foto 620).

Encontramos en el exterior 2 focos ahorrativos (foto, 637,638), y 5 lámparas Florecentes (Foto  635, 636).

El Mini  market 2002 pertenece a una casa de dos pisos y una terraza (foto 621), la terraza se encuentra en el ultimo piso, es baldosa pegada con cemento (foto 630), con una área de 170 metros cuadrados, y encontramos un cuadrado hecho de cemento de 72 metros cuadrados (Foto629) este lo hicieron ya que anterior mente filtraba agua a los departamentos de abajo .Este es un buen sitio para instalar paneles solares. Se encontraron unos alambres amarrados en un tubo (foto631).

El medidor esta cubierto y los alambres en orden( foto 615).

Nota

- El Mini Marquek 2002 esta bien adecuado, el toldo de zinc da mucha sombra al lugar por lo cual la tienda es fresca.

- No tienen aire acondicionado, ya que el lugar es fresco.

- La altura total del edificio es de 12 metros, pero tome el  calculo para sacar  las fachadas, de 3,37 metros que es la altura de la tienda que tiene.

# A. Building configuration

| Construction year | 1991 |
| --- | --- |
| Orientation of main entrance | Este |

Density of nearby obstructions

| ( Very dense | X Moderately dense | ( Few buildings | ( Free standing |
| --- | --- | --- | --- |

Height of surrounding buildings:

| ( Higher | ( Same | X Shorter | ( Variable |
| --- | --- | --- | --- |

Building’s Shape:

| X Rombo | X Rectangular | ( Square with Atrium |
| --- | --- | --- |

External Walls colour 		( dark		X medium	( light

Roof colour 			( dark		( medium	X light

| Yearly Energy consumption 01 del 2002 al 07 2003 |
| --- |
| Electricity (kWh) Annual bill: | 45300 Kw $5948.57 |

Annual operation:	from month    1  to month  12   month off       .

Heating period:		from month      to month         .

Cooling period:		from month      to month      .

# B. Description of envelope construction

# B1.    Facade

Attention: All shading percentages below are related to total window area.

|  | Facade 1 | Facade 2 | Facade 3 | Facade 4 |
| --- | --- | --- | --- | --- |
| Facade orientation | Este | Norte | Oeste | Sur |
| Facade Area (m²) | 42 | 47 | 42 | 47 |
| Walls U-value [W/(m²K)] | hecho | de | cemento | toda el edificio |
| Windows area, % of facade area | 17%/ 7 | 17%/8 | 0 | 0 |
| Percentage of natural shading (%) | 0 | 0 | 0 | 0 |
| Percentage of external vertical blinds (%) | 17% | 17% | 0 | 0 |
| Percentage of external louvers (%) | 0 0 | 0 0 | 0 0 | 0 0 |
| Percentage of overhangs (%) | 0 | 0 | 0 | 0 |
| Percentage of awnings (%)Toldo de cing medida de Largo x ancho | 20 m | 0 0 | 0 0 | 0 0 |
| Percentage of side fins (%) | 0 | 0 | 0 | 0 |
| Percentage of shutters (%) | 0 | 0 | 0 | 0 |
| Percentage of internal vertical blinds (%) | 0 | 0 | 0 | 0 |
| Percentage of internal louvers (%) | 0 | 0 | 0 | 0 |

# B2.    Floor

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Floor area on the ground | 166 | Esta hecho de cemento, pegado con piedras y tiene baldosas |
| Floor over non-heated zone | 0 | 0 |
| Floor exposed to the exterior (pilotis) | 0 | 0 |

# B3.    Roof

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Exposed roof area/ el Techo del edificio | 170 | Es de cemento y en la mitad encontramos otro cuadrado de cemento de 72 metros cuadrados |
| Roof area to non heated spaces | 0 | 0 |
| Roof glazed area | 0 | 0 |

#### C.    General inputs

| Parameter | Value | Description |
| --- | --- | --- |
| Site area, m² | 166 | Total lot area |
| Area of foundations, m² | 166 | Area of typical floor |
| Green Areas, m² | 0 | Green Areas |
| Height of typical floor, m | 3.47 | Height of typical floor |
| Number of floors | 1 | Number of floors, ground floor included. |
| Number of basement floors | 0 | Number of floors, below ground floor. |
| Number of rooms | 2 | Number of rooms |
| Number of staircases | 0 | Number of internal staircases |
| Gross floor area, m² | 166 | Gross floor area (basement included) |
| Garage area, m² | 0 | Garage area in basement |
| Heated floor area, m² | 0 | Heated floor area |
| Conditioned area, m² | 0 | Conditioned area |
| Supply air flow rate in rooms, m3/h | 0 | Supply air flow in rooms |
| Installed heating power, kW (Thermal) | 0 | Installed heating power |
| Installed cooling power (thermal), kW | 0 | Installed cooling power (thermal) |
| Installed electrical cooling power | 0 |  |

#### D.   Inputs for heating / cooling

| Heating set point, °C | 0 | The internal temperature is the set point temperature during the heating season. |
| --- | --- | --- |
| Cooling set point, °C | 0 | The internal temperature is the set point temperature during the cooling season. |
| Temperature control | 0 | 1: Bad control (No thermostatic control and no night set back, regulary overheating during winter) 2. No control (No thermostatic control and no night set back) 3. Standard (Thermostatic control of the indoor temperature during the heating season OR night set back of 3 °C) 4. Good control (Thermostatic control AND night setback of up to 3 °C during the heating season) 5. Advanced control (Probabilistic control of the heating system based on an estimated weather forecasts and adapted user behaviour) |
| Infiltration, ach | 0 | 1. 0.1ach 2. 0.5 ach 3. 1 ach 4. 1.5 ach |
| Boiler efficiency, % | 0 | 1. Low efficiency (Boiler in poor stage. Insulation of boiler and storage is missing. Boiler room and pipes in the boiler room are not insulated) 2. Under medium efficiency (Boiler is more than 15 years old or in a poor condition of maintenance. Insulation level of boiler and storage is insufficient) 3. Medium (Boiler is less than 15 years old OR in perfect condition. Insulation level of boiler and storage is sufficient.) 4. Over medium efficiency (Boiler is less than 15 years old and in perfect condition. Insulation level of boiler and storage is sufficient.) |
| Number of existing ceiling fans | 0 | Number of existing ceiling fans |

#### E.  Inputs for hot water production

| Fuel for domestic hot water production | 0 | 1: oil, 2:gas, 3: electricity |
| --- | --- | --- |
| Solar collectors surface, m2 | 170 |  |
| Available space for additional solar collectors, m2 | 170 | Es un espacio super grande y se puede ubicar en toda la area |

Available space towards south, for solar collectors:

| X | ( | ( |  |
| --- | --- | --- | --- |

#### Inputs for artificial lighting

|  | Internal type | External type | Power (Watt) | Daily use (h) | Remark |
| --- | --- | --- | --- | --- | --- |
| Type of existing lamps 1: standard incandescent, 2: efficient incandescent, 3: tube fluorescent, 4: compact fluorescent, 5: discharge, 6:other/ Ahorradores | 0 0 5 0 | 0 0 5 2 | 0 0 40 3kw | 0 0 5 horas diarias 5 horas diarias | 0 0 |

#### Inputs for electric CONSUMPTION

LOCALITY : Av . Charles Darwin y av. malville

N. OF PERSON: 1

| Contract typology: Residential Commercial Industrial Other | Type of fee: $ 310.19 |
| --- | --- |
| Power (kW) Voltage (V): 110 Frequency (Hz): Safety equipments: | Consumption (kWh/year) |

| Person | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21/22 | 22/23 | 23/24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Plants-Equipments hours | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21-22 | 22-23 | 23-24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lighting (W) |  |  |  |  |  |  |  |  |  |  |  |  | xx | xx | xx | xx | xx |  |  |
| Fan (W) |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Food Refrigerator (W) |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Hot Water (W) |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Cooling (W) |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

HOUSEHOLD APPLIANCE

|  | Number | Power (Watt) | Total Daily use(h) | Hour of use | Remark |
| --- | --- | --- | --- | --- | --- |
| Radio/ Television | 1 1 | 88kw 85 kw | 6 dias / 1 hora diaria 6 dias/2 horas diarias | 6 12 |  |
| Computer | 0 | 0 | 0 | 0 | 0 |
| Domestic refrigerator |  |  |  |  |  |
| Freezer/ congelador | 2 |  | 7 dias/ 24 h | 168 c/u | viejos |
| Ceiling fan | 0 | 0 | 0 | 0 | 0 |
| Washing machine | 0 | 0 | 0 | 0 | 0 |
| Electrical space heating | 0 | 0 | 0 | 0 | 0 |
| Electrical DHW | 0 | 0 | 0 | 0 | 0 |
| Other Camara de Frio Camaras de ambiente Maquina Registradora | 1 2 1 |  | 7 dias/ 24 h 7 dias/ 24 h 6 dias | 168 c/u 168 c/u 68 h | Nuevos |
| Kitchen : Cooking set Oven | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 |
| AC system 1) Split system 2) HVAC | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 |