# INPUTS CHECKLIST COMMERCIAL

# tarifa OFICIAL codigo 683 n# medidor 6622231

# (Foto 583)

La estación de policía se encuentra Av.Española y Charles Darwin, es la calle principal y muy transitada.

Se encuentra rodean de pocas edificaciones, la altura de la edificación es mas alta que los edificios que le rodean.

Tiene forma rectangular y la fachada principal se encuentra orientada al Sur (foto 585, 586), al ingresar podemos observar puertas de vidrio transparente, suelo de baldosa y el techo es losa

(Cemento). El edificio tiene 2 plantas en la de abajo encontramos 5 oficinas las cuales tienen vidrios transparentes con persianas que cubre del sol (foto 594, 506).cada oficina tiene sus equipos de trabajo como computadoras, calculadoras, impresoras, fax, radios de comunicación ( Foto 498,476, 479,487,488,492,497,499,502) y también encontramos aires acondicionados los cuales solo lo usan en época de calor que es de Dic a Mayo, estos aires acondicionados no tienen marca ni datos de lo que se consume en KW , (Foto 508, 503, 513). Las instalaciones no son muy buenas ( Foto 485), luego subimos por 2 escalones y llegamos a una sala de espera( Foto 519, 520) donde observamos piso de baldosa con paredes de cemento y una puerta de vidrio transparente donde da luz.

Pasamos a mano izquierada a la oficina de secretaria, un cuarto angosto de paredes de cemento con una ventana cubierta con una cortina para proteger del sol, ( foto 513, 514, 515). A mano de recha esta la oficina del comandante es una lugar amplio con ventanas grandes con persianas piso de baldosa con techo de losa( foto 510, 518)., luego salimos y subimos por dos escaleras de madera(580) y arriba nuestro podemos observar una entrada de luz natural puesta un techo y con vidrios a los lados y cuando se abre pasa mucha brisa( Foto 522. 523, 579), luego abrimos una puerta de hierro y salimos a la terraza donde podemos observar la antena que usan para la radios(Foto 483), tanques de Agua( Foto 482) conexiones en el piso( foto 483) es una terraza grande que da la vista al mar y el sol pega muy fuerte es techo de losa ( cemento y seria una buena opción para los paneles solares( Foto 481).

# A. Building configuration

| Construction year | 1973 |
| --- | --- |
| Orientation of main entrance | Sur |

Density of nearby obstructions

| ( Very dense | ( Moderately dense | X Few buildings | ( Free standing |
| --- | --- | --- | --- |

Height of surrounding buildings:

| ( Higher | ( Same | X Shorter | ( Variable |
| --- | --- | --- | --- |

Building’s Shape:

| ( Square | X Rectangular | ( Square with Atrium |
| --- | --- | --- |

External Walls colour 		( dark		( medium	X light

Roof colour 			( dark		X medium	( light

| Yearly Energy consumption 01 DEL 2002 AL 07 DEL 2003 |
| --- |
| Electricity (kWh) Annual bill: | 44745 kw $ 5065.94 |

Annual operation:	from month   1   to month  12   month off       .

Heating period:		from month      to month         .

Cooling period:		from month      to month      .

# B. Description of envelope construction

# B1.    Facade

Attention: All shading percentages below are related to total window area.

|  | Facade 1 | Facade 2 | Facade 3 | Facade 4 |
| --- | --- | --- | --- | --- |
| Facade orientation | Sur | Oeste | Norte | Este |
| Facade Area (m²) | 52 | 37 | 52 | 37 |
| Walls U-value [W/(m²K)] | bloque columna | de | cemento armado | con |
| Windows area, % of facade area | 33/63% | 22/59% | 0 | 0 |
| Percentage of natural shading (%) | 0 | 0 | 0 | 0 |
| Percentage of external vertical blinds (%) | 0 | 0 | 0 | 0 |
| Percentage of external louvers (%) | 0 | 0 | 0 | 0 |
| Percentage of overhangs (%) | 0 | 0 | 0 | 0 |
| Percentage of awnings (%) | 0 | 0 | 0 | 0 |
| Percentage of side fins (%) | 0 | 0 | 0 | 0 |
| Percentage of shutters (%) | 0 | 0 | 0 | 0 |
| Percentage of internal vertical blinds (%) | 0 | 0 | 0 | 0 |
| Percentage of internal louvers (%) | 100% | 100% | 0 | 0 |

# B2.    Floor

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Floor area on the ground | 221 | Cemento con baldosa |
| Floor over non-heated zone | 0 | 0 |
| Floor exposed to the exterior (pilotis) | 0 | 0 |

# B3.    Roof

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Exposed roof area | 221 | cemento |
| Roof area to non heated spaces | 0 | 0 |
| Roof glazed area | 0 | 0 |

#### C.    General inputs

| Parameter | Value | Description |
| --- | --- | --- |
| Site area, m² | 221 | Total lot area |
| Area of foundations, m² | 221 | Area of typical floor |
| Green Areas, m² | 0 | Green Areas |
| Height of typical floor, m | 3 | Height of typical floor |
| Number of floors | 2 | Number of floors, ground floor included. |
| Number of terraza | 1 | Number of floors, below ground floor. |
| Number of rooms/ oficinas | 8 | Number of rooms |
| Number of staircases | 4 | Number of internal staircases |
| Gross floor area, m² | 221 | Gross floor area (basement included) |
| Garage area, m² | 0 | Garage area in basement |
| Heated floor area, m² | 0 | Heated floor area |
| Conditioned area, m² | 0 | Conditioned area |
| Supply air flow rate in rooms, m3/h | 00 | Supply air flow in rooms |
| Installed heating power, kW (Thermal) | 0 | Installed heating power |
| Installed cooling power (thermal), kW | 5 | Installed cooling power (thermal) Solo usan en época de calor Dic -May |
| Installed electrical cooling power | 0 |  |

#### D.   Inputs for heating / cooling

| Heating set point, °C | 0 | The internal temperature is the set point temperature during the heating season. |
| --- | --- | --- |
| Cooling set point, °C | 0 | The internal temperature is the set point temperature during the cooling season. |
| Temperature control | 0 | 1: Bad control (No thermostatic control and no night set back, regulary overheating during winter) 2. No control (No thermostatic control and no night set back) 3. Standard (Thermostatic control of the indoor temperature during the heating season OR night set back of 3 °C) 4. Good control (Thermostatic control AND night setback of up to 3 °C during the heating season) 5. Advanced control (Probabilistic control of the heating system based on an estimated weather forecasts and adapted user behaviour) |
| Infiltration, ach | 0 | 1. 0.1ach 2. 0.5 ach 3. 1 ach 4. 1.5 ach |
| Boiler efficiency, % |  | 1. Low efficiency (Boiler in poor stage. Insulation of boiler and storage is missing. Boiler room and pipes in the boiler room are not insulated) 2. Under medium efficiency (Boiler is more than 15 years old or in a poor condition of maintenance. Insulation level of boiler and storage is insufficient) 3. Medium (Boiler is less than 15 years old OR in perfect condition. Insulation level of boiler and storage is sufficient.) 4. Over medium efficiency (Boiler is less than 15 years old and in perfect condition. Insulation level of boiler and storage is sufficient.) |
| Number of existing ceiling fans | 2 | Number of existing ceiling fans |

#### E.  Inputs for hot water production

| Fuel for domestic hot water production |  | 1: oil, 2:gas, 3: electricity |
| --- | --- | --- |
| Solar collectors surface, m2 |  |  |
| Available space for additional solar collectors, m2 | 221 | Aqui podemos encontrar una terraza de cemento fundido |

Available space towards south, for solar collectors:

| X | ( | ( |  |
| --- | --- | --- | --- |

#### Inputs for artificial lighting

|  | Internal type | External type | Power (Watt) | Daily use (h) | Remark |
| --- | --- | --- | --- | --- | --- |
| Type of existing lamps 1: standard incandescent, 2: efficient incandescent, 3: tube fluorescent, 4: compact fluorescent, 5: discharge, 6:other: Ahorrativos | Tipo/N#/KW 1/11/60 -100 3/1/20 4/4/ 40 6/2/3 | Tipo/N#/KW | 60 a 100 20 40 3 | 7 H 7H 7H 7 H |  |

#### Inputs for electric CONSUMPTION

LOCALITY : AV ESPAÑOLA Y CHARLES DARWIN

N. OF PERSON: 13 PERSONAS QUE TRABAJAN

| Contract typology: Residential Commercial Industrial Other Oficial | Type of fee: $349.27 |
| --- | --- |
| Power (kW) Voltage (V): 110 -240 Frequency (Hz): 60 Safety equipments: | Consumption (kWh/year) |

| Person | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21/22 | 22/23 | 23/24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Horas de trabajo |  |  | XX | XX | XX | XX | XX | XX |  | X | XX | XX |  |  |  |  |  |  |  |

| Plants-Equipments hours | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21-22 | 22-23 | 23-24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lighting (W) |  |  | XX | XX | XX | XX | XX | XX |  | X | XX | XX |  |  |  |  |  |  |  |
| Fan (W) |  |  | XX | XX | XX | XX | XX | XX |  | X | XX | XX |  |  |  |  |  |  |  |
| Food Refrigerator (W) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Hot Water (W) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| Cooling (W) |  |  | XX | XX | XX | XX | XX | XX |  | X | XX | XX |  |  |  |  |  |  |  |

Nota los fan, y coling solo lo utilizan en epoca de calor de Dic a Mayo en el año

HOUSEHOLD APPLIANCE

|  | Number | Power (Watt) | Total Daily use(h) | Hour of use | Remark |
| --- | --- | --- | --- | --- | --- |
| Radio Television | 4 1 | 25 w 85 w | Lunes a Vernes Lunes a viernes | 5 h 1 h |  |
| Computer Impresoras Impresora epson fx 1180 Telefax Calculadoras Electricas Escaner Fotocopiadora Maquina de escribir Radio de Comucicacion icom Radio de comunicacion Motorola Ventilador | 8 7 1 5 2 1 1 1 1 1 1 | 120 w 72 w 72 w 9.9 w 13200 w 950 w 37.2 w 165.6 w 3840 w | Lunes a Viernes Lunes a Viernes Lunes a Viernes Lunes a Viernes Lunes a Viernes Debes en cuando Lunes a Viernes Lunes a Viernes Lunes a Domingo Lunes a domingo Lunes a Viernes | 6 H 0:15 min 0:15 min 6H 1 h 0:15 min 2 H 1 h 24 h 24 h 10 h | Solo en epoca de calor |
| Domestic refrigerator | 0 | 0 | 0 | 0 | 0 |
| Freezer | 0 | 0 | 0 | 0 | 0 |
| Ceiling fan | 2 |  | Lunes a viernes | 10h | Solo en época de calor |
| Washing machine | 0 | 0 | 0 | 0 | 0 |
| Electrical space heating | 0 | 0 | 0 | 0 | 0 |
| Electrical DHW | 0 | 0 | 0 | 0 | 0 |
| Other (cafeteras, sambuchera) | 0 | 0 | 0 | 0 | 0 |
| Kitchen : Cooking set Oven | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 |
| AC system 1) Split system 2) HVAC | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 |