# INPUTS CHECKLIST RESIDENTIAL HOUSE

# sra. jacqueline vazquez

# tarifa residencial codigo n# 461 medidor 245036(Foto 894,850)

La residencia de la Sra. Jacqueline Vázquez  se encuentra ubicada en la Avenida principal  Charles Darwin, tiene una moderately dense Obstruncions, la altura que tiene es similar a las otras edificaciones que le rodean, tiene forma cuadrada, el color de sus paredes son claras, y el techo es medio claro porque es losa de cemento.

Esta residencial es de tres pisos( foto 852) el primero esta alquilado para negocios como de shop, cafetería y central telefónica cada uno de los negocios tiene su medidor, en el segundo piso encontramos una galería de Arte, y en el tercer piso subiendo por las escaleras de italpiso(foto 853), encontramos a primera vista una puerta grande con ventanas( foto 839) donde te comunica para ir   a una de las habitaciones que esta Ubicada en el Techo de la casa( Foto 827) es de bloque de cemento , techo es de cemento y el piso de baldosa ( Foto 831) con una temperatura promedio de 22°c.

Luego bajamos las gradas(Foto 837) que son de cemento con baldosa, y ingresamos a la sala( foto 838) tiene 19m2, el piso es de baldosa, y sus paredes de bloque con cemento la temperatura promedio aquí es de 22 °c, luego  a mano derecha tenemos el comedor( Foto 840) que es al aire libre con vista al mar, tiene un toldo blanco con una temperatura promedio de 29°c, el piso de baldosa con 24°c, y las paredes de bloque con 24°c.

Después del comedor encontramos la segunda habitación ( foto 841) tenemos una puerta de madera grande con vidrios, y al abrir nos encontramos con un falcón vista al mar, dos ventanas de madera a los lados donde ventila la habitación, , el techo cerca de la terraza antes de salir, podemos ver que es de madera y techo de teja, luego encontramos en la misma habitación el techo de losa, con paredes de bloque de cemento y piso de baldosa con una temperatura promedio de 23°c la habitación, incluye el baño, que tiene ducha eléctrica( Foto 843).

Luego ingresamos a la tercera habitación  ( foto 844, 845) donde tiene una puerta grande de vidrio, con cortinas blancas, el techo es de losa y el piso italpiso, y sus paredes de bloque de cemento la temperatura promedio  es de 23°c a 24°c, luego ingresamos al estudio( Foto 847) donde se observa en la parte posterior vidrios transparentes (  foto 848 ) piso de italpiso, techo de losa, y paredes de bloque de cemento, temperatura promedio de 22°c.

Luego ingresamos a la cocina (foto 846)  y al frente encontramos otra ventana transparente con cortinas, tiene 9 metros cuadrados , piso de cerámica, techo de losa, paredes de bloque de cemento, la temperatura promedio es de 23°c., luego por el estudio a mano derecha encontramos un baño con ducha electrica(foto 857) que nos conecta a la habitación cuatro( Foto 854, 855) mide 18 metros cuadrados, el techo es de losa, el piso es de italpiso, encontramos al frente una ventana grande de vidrios transparentes y con cortinas, tiene un pequeño corredor que nos comunica a la otra puerta que nos lleva para salir de la casa.

El techo es de losa de cemento y aquí encontramos la cúpula, y tiene una linda vista a todo el pueblo, aquí se podría dar la opción de paneles solares ( foto 832, 833, 834, 835).

Nota

- Esta residencia esta dentro del Plan piloto de alojamiento en hogares donde puede recibir turistas, y su capacidad es de 3 pasajeros.

- El medidor esta lleno de cables y no están en una caja que los proteja.

- Se encuentra una sola mala instalación en el sector del techo (foto 836).

# A. Building configuration

| Construction year | 1992 |
| --- | --- |
| Orientation of main entrance | Oeste |

Density of nearby obstructions

| ( Very dense | X Moderately dense | ( Few buildings | ( Free standing |
| --- | --- | --- | --- |

Height of surrounding buildings:

| ( Higher | X Same | ( Shorter | ( Variable |
| --- | --- | --- | --- |

Building’s Shape:

| X Square | ( Rectangular | ( Square with Atrium |
| --- | --- | --- |

External Walls colour 		( dark		( medium	X light

Roof colour 			( dark		( medium	X light

| Energy consumption 01 del 2002 al 07 del 2003 |
| --- |
| Electricity (kWh): or Annual bill | 2381 KW $ 1494.13 |

Heating period:		from month   6   to month       11  .

Cooling period:		from month   12   to month  5    .

# B. Description of envelope construction

# B1.    Facade

Attention: All shading percentages below are related to total window area.

|  | Facade 1 | Facade 2 | Facade 3 | Facade 4 |
| --- | --- | --- | --- | --- |
| Facade orientation | Oeste | Norte | Este | Sur |
| Facade Area (m²) | 109 m² | 135 m² | 109 m² | 135 m² |
| Walls U-value [W/(m²K)] | Bloque | de | cemen | to |
| Windows area, % of facade area | 13/12% | 0 | 3/3% | 3/4% |
| Percentage of natural shading (%) | 0 | 0 | 0 | 0 |
| Percentage of external vertical blinds (%) | 4% | 0 | 0 | 0 |
| Percentage of external louvers (%) | 0 | 0 | 0 | 0 |
| Percentage of overhangs (%) | 0 | 0 | 0 | 0 |
| Percentage of awnings (%) Toldo | 3% | 0 | 0 | 0 |
| Percentage of side fins (%) | 0 | 0 | 0 | 0 |
| Percentage of shutters (%) | 0 | 0 | 0 | 0 |
| Percentage of internal vertical blinds (%) CORTINAS | 30% | 5% | 10% | 10% |
| Percentage of internal louvers (%) | 0 | 0 | 0 | 0 |

Nota: el área esta calculada por todo el edificio, lo que corresponde al tercer piso y es la casa esta calculado los %

# B2.    Floor

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Floor area on the ground | 299m2 | Es el área del edificio total y es de cemento con italpiso |
| Floor over non-heated zone | 0 | 0 |
| Floor exposed to the exterior (pilotis) | 0 | 0 |

# B3.    Roof

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Exposed roof area | 139m2 | El techo es de losa de cemento |
| Roof area to non heated spaces | 0 | 0 |
| Roof glazed area | 0 | 0 |

#### C.    General inputs

| Parameter | Value | Description |
| --- | --- | --- |
| Site area, m² | 438, m² | Total lot area |
| Area of foundations, m² | 299, m² | Area of typical floor |
| Green Areas, m² | 0 | Green Areas |
| Height of typical floor, m | 7m | Height of typical floor |
| Number of floors | 3 | Number of floors, ground floor included. El tercer piso es la casa |
| Number of basement floors | 0 | Number of floors, below ground floor. |
| Number of rooms | 4 | Number of rooms |
| Number of staircases | 4 | Number of internal staircases |
| Gross floor area, m² | 438, m² | Gross floor area (basement included) |
| Garage area, m² | 0 | Garage area in basement |
| Heated floor area, m² | 0 | Heated floor area |
| Conditioned area, m² | 0 | Conditioned area |
| Supply air flow rate in rooms, m3/h | 0 | Supply air flow in rooms |
| Installed heating power, kW (Thermal) | 0 | Installed heating power |
| Installed cooling power (thermal), kW | 0 | Installed cooling power (thermal) |
| Installed electrical cooling power | 1 | Aire acondicionado 1474w |

#### D.   Inputs for heating / cooling

| Heating set point, °C | 0 | The internal temperature is the set point temperature during the heating season. |
| --- | --- | --- |
| Cooling set point, °C | 0 | The internal temperature is the set point temperature during the cooling season. |
| Temperature control | 0 | 1: Bad control (No thermostatic control and no night set back, regulary overheating during winter) 2. No control (No thermostatic control and no night set back) 3. Standard (Thermostatic control of the indoor temperature during the heating season OR night set back of 3 °C) 4. Good control (Thermostatic control AND night setback of up to 3 °C during the heating season) 5. Advanced control (Probabilistic control of the heating system based on an estimated weather forecasts and adapted user behaviour) |
| Infiltration, ach | 0 | 1. 0.1ach 2. 0.5 ach 3. 1 ach 4. 1.5 ach |
| Boiler efficiency, % | 1 | 1. Low efficiency (Boiler in poor stage. Insulation of boiler and storage is missing. Boiler room and pipes in the boiler room are not insulated) 2. Under medium efficiency (Boiler is more than 15 years old or in a poor condition of maintenance. Insulation level of boiler and storage is insufficient) 3. Medium (Boiler is less than 15 years old OR in perfect condition. Insulation level of boiler and storage is sufficient.) 4. Over medium efficiency (Boiler is less than 15 years old and in perfect condition. Insulation level of boiler and storage is sufficient.) |
| Night ventilation techniques | 0 | Night ventilation techniques (put 1 if it is used and 0 if not) |
| Number of existing ceiling fans | 0 | Number of existing ceiling fans |

#### E.  Inputs for hot water production

| Fuel for domestic hot water production | 0 | 1: oil, 2:gas, 3: electricity |
| --- | --- | --- |
| Solar collectors surface, m2 | 0 |  |
| Available space for additional solar collectors, m2 | 9m² | Es techo de Losa |

Available space towards south, for solar collectors:

| ( | ( | X |  |
| --- | --- | --- | --- |

#### Inputs for artificial lighting

|  | Internal type | External type | Power (Watt) | Daily use (h) | Remark |
| --- | --- | --- | --- | --- | --- |
| Type of existing lamps 1: standard incandescent, 2: efficient incandescent, 3: tube fluorescent, 4: compact fluorescent, 5: discharge, 6:other Ahorrador lamparas lamparas | 19 1 3 3 | 4 3 | 60W 20w 60w 30w | 5H 5h 5h 1h | Mas en la noche |

#### Inputs for electric CONSUMPTION

LOCALITY : Av Charles Darwin

N. OF PERSON: 4 personas

| Contract typology: Residential Commercial Industrial Other | Type of fee: $ 30.92 |
| --- | --- |
| Power (kW) Voltage (V): 110 Frequency (Hz):60 Safety equipments: | Consumption (kWh/year) KW 6922 or annual bill $ 809.13 |

| Person | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21/22 | 22/23 | 23/24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Plants-Equipments hours | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21-22 | 22-23 | 23-24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lighting (W) |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | X | XX | XX | XX | XX | XX | 0 |
| Fan (W) |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  |
| Food Refrigerator (W) |  | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX |
| Hot Water (W) |  | 0 | X | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Cooling (W) |  | 0 | 0 | 0 | 0 | 0 | 0 | XX | XX | XX | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

Nota: Las luces  se utilizan a partir de las 6:30 pm hasta las 11pm, el aire acondicionado solo se utiliza a partir de Diciembre a Mayo

HOUSEHOLD APPLIANCE

|  | Number | Power (Watt) | Total Daily use(h) | Hour of use | Remark |
| --- | --- | --- | --- | --- | --- |
| Radio Television Television | 1 1 1 | 5w 175w 85w | Todos los dias Todos los dias Todos los dias | 24h 6h 3h |  |
| Computer Impresora telefax | 1 1 1 | 165w 44w 72w | Lunes a Viernes Todos los dias Todos los dias | 30 min 2min 24h | Siempre conectado |
| Domestic refrigerator | 1 | 740w | Todos los dias | 24h |  |
| Freezer | 0 | 0 | 0 | 0 |  |
| Ceiling fan | 0 | 0 | 0 | 0 |  |
| Iron | 1 | 36w | Una vez semana | 15min |  |
| Washing machine | 1 | 520w | 3 veces a la semana | 20 min |  |
| Electrical space heating | 0 | 0 | 0 | 0 | 0 |
| Electrical DHW | 0 | 0 | 0 | 0 | 0 |
| Other Olla arrosera Sambuchera licuadora | 1 1 1 | 800w 700w 450w | Todos los dias Todos los dias Todos los dias | 30 minutos 3 min 5 min |  |
| Kitchen : Cooking set Oven |  |  |  |  |  |
| AC system 1) Split system 2) Centralised HVAC Aire acondicionado | 1 | 1474w | Diembre a Mayo | 3h |  |