# INPUTS CHECKLIST INDUSTRIA

# BLOQUERIA INSULAR DE CEMENTO

# tarifa iNDUSTRIAL codigo 498 n# medidor 445244 (Foto 306 )

# La Bloquearía insular de Galápagos se encuentra ubicada en el Barrio las Peñas Bajas, es un barrio tranquilo y no hay mucho movimiento de trafico.  Rodeado de edificios  tiene una altura variable con referencia a las otras edificaciones tiene forma cuadrada, el color de las paredes es gris, no tiene techo, el único que tiene es para cubrir la maquinaria que utilizan para hacer el bloque, este techo esta en mal estado (Foto 295), y hay alambres que cruzan por  todo lado (Foto  300,301,) mala instalación eléctrica (Foto 303).

# En la Fachada 3 podemos encontrar un cuarto donde guardan los materiales para hacer el Bloque, este esta hecho de bloque y pegado con cemento, y el techo es de ternil(Foto 291)

# Las Maquinarias que utilizan para hacer el Bloque esta ubicada en la fachada 2(Foto 291), esta maquinaria la llaman motores monofásicos , utilizan dos para hacer el bloque, son aparatos muy viejos y con alambres descubiertos ( Foto 296, 298,  299, 304).

# Donde encontramos el medidor esta la caja de breaks sin tapa y todos los alambres descubiertos (Foto 288, 306).

# Nota:

# La bloquearía no tiene un techo para poner los paneles solares, pero se podría instalar en la fachada 3, donde se podría construir un armazón para los paneles.( Foto 292).

# Aquí no tienen ni focos, ni radios, ni televisiones, solo los equipos para hacer los bloques.

# No tienen ningún tipo de sombra que cubra el lugar.

# A. Building configuration

| Construction year | 1988 |
| --- | --- |
| Orientation of main entrance | NorEste |

Density of nearby obstructions

| X Very dense | ( Moderately dense | ( Few buildings | ( Free standing |
| --- | --- | --- | --- |

Height of surrounding buildings:

| ( Higher | ( Same | ( Shorter | X Variable |
| --- | --- | --- | --- |

Building’s Shape:

| X Square | ( Rectangular | ( Square with Atrium |
| --- | --- | --- |

External Walls colour 		( dark		X medium	( light

Roof colour 			X dark		( medium	( light

| Yearly Energy consumption 01 del 2002 al 07 del 2003 |
| --- |
| Electricity (kWh) Annual bill: | 7595 Kw $ 750.33 |

Annual operation:	from month    1  to month  12   month off       .

Heating period:		from month      to month         .

Cooling period:		from month      to month      .

# B. Description of envelope construction

# B1.    Facade

Attention: All shading percentages below are related to total window area.

|  | Facade 1 | Facade 2 | Facade 3 | Facade 4 |
| --- | --- | --- | --- | --- |
| Facade orientation | Norte | Noreste | Sureste | Suroeste |
| Facade Area (m²) | 50 | 41 | 50 | 41 |
| Walls U-value [W/(m²K)] | bloque | de de | cemento ripio | piso |
| Windows area, % of facade area | 0 | 0 | 0 | 0 |
| Percentage of natural shading (%) | 0 | techo cubre equipos | 0 | 0 |
| Percentage of external vertical blinds (%) | 0 | 0 | 0 | 0 |
| Percentage of external louvers (%) | 0 | 0 | 0 | 0 |
| Percentage of overhangs (%) | 0 | 0 | 0 | 0 |
| Percentage of awnings (%) | 0 | 0 | 0 | 0 |
| Percentage of side fins (%) | 0 | 0 | 0 | 0 |
| Percentage of shutters (%) | 0 | 0 | 0 | 0 |
| Percentage of internal vertical blinds (%) | 0 | 0 | 0 | 0 |
| Percentage of internal louvers (%) | 0 | 0 | 0 | 0 |

# B2.    Floor

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Floor area on the ground | 263 | Piso de ripio |
| Floor over non-heated zone | 0 | 0 |
| Floor exposed to the exterior (pilotis) | 0 | 0 |

# B3.    Roof

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Exposed roof area | 41 | Techo de ternil Cubre maquinaria |
| Roof area to non heated spaces | 0 | 0 |
| Roof glazed area | 0 | 0 |

#### C.    General inputs

| Parameter | Value | Description |
| --- | --- | --- |
| Site area, m² | 263 | Total lot area |
| Area of foundations, m² | 263 | Area of typical floor |
| Green Areas, m² | 0 | Green Areas |
| Height of typical floor, m | 2.80 | Height of typical floor |
| Number of floors | 1 | Number of floors, ground floor included. |
| Number of basement floors | 0 | Number of floors, below ground floor. |
| Number of rooms | 1 | Number of rooms |
| Number of staircases | 0 | Number of internal staircases |
| Gross floor area, m² | 0 | Gross floor area (basement included) |
| Garage area, m² | 0 | Garage area in basement |
| Heated floor area, m² | 0 | Heated floor area |
| Conditioned area, m² | 0 | Conditioned area |
| Supply air flow rate in rooms, m3/h | 0 | Supply air flow in rooms |
| Installed heating power, kW (Thermal) | 0 | Installed heating power |
| Installed cooling power (thermal), kW | 0 | Installed cooling power (thermal) |

#### D.   Inputs for heating / cooling

| Heating set point, °C | 0 | The internal temperature is the set point temperature during the heating season. |
| --- | --- | --- |
| Cooling set point, °C | 0 | The internal temperature is the set point temperature during the cooling season. |
| Temperature control | 0 | 1: Bad control (No thermostatic control and no night set back, regulary overheating during winter) 2. No control (No thermostatic control and no night set back) 3. Standard (Thermostatic control of the indoor temperature during the heating season OR night set back of 3 °C) 4. Good control (Thermostatic control AND night setback of up to 3 °C during the heating season) 5. Advanced control (Probabilistic control of the heating system based on an estimated weather forecasts and adapted user behaviour) |
| Infiltration, ach | 0 | 1. 0.1ach 2. 0.5 ach 3. 1 ach 4. 1.5 ach |
| Boiler efficiency, % | 0 | 1. Low efficiency (Boiler in poor stage. Insulation of boiler and storage is missing. Boiler room and pipes in the boiler room are not insulated) 2. Under medium efficiency (Boiler is more than 15 years old or in a poor condition of maintenance. Insulation level of boiler and storage is insufficient) 3. Medium (Boiler is less than 15 years old OR in perfect condition. Insulation level of boiler and storage is sufficient.) 4. Over medium efficiency (Boiler is less than 15 years old and in perfect condition. Insulation level of boiler and storage is sufficient.) |
| Number of existing ceiling fans | 0 | Number of existing ceiling fans |

#### E.  Inputs for hot water production

| Fuel for domestic hot water production | 0 | 1: oil, 2:gas, 3: electricity |
| --- | --- | --- |
| Solar collectors surface, m2 | 0 |  |
| Available space for additional solar collectors, m2 | 50 | Fachada 3, opción de instalar o hacer una base paneles |

Available space towards south, for solar collectors:

| ( | ( | X |  |
| --- | --- | --- | --- |

#### Inputs for artificial lighting

|  | Internal type | External type | Power (Watt) | Daily use (h) | Remark |
| --- | --- | --- | --- | --- | --- |
| Type of existing lamps 1: standard incandescent, 2: efficient incandescent, 3: tube fluorescent, 4: compact fluorescent, 5: discharge, 6:other | 0 0 0 0 0 0 | 0 0 0 0 0 0 | 0 0 0 0 0 0 | 0 0 0 0 0 0 | 0 0 0 0 0 0 |

#### Inputs for electric CONSUMPTION

LOCALITY : Calle Peñas Bajas

N. OF PERSON: 2

| Contract typology: Residential Commercial Industrial Other | Type of fee: $ 22.82 |
| --- | --- |
| Power (kW) Voltage (V): Frequency (Hz): Safety equipments: | Consumption (kWh/year) |

| Person | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21/22 | 22/23 | 23/24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Plants-Equipments hours | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21-22 | 22-23 | 23-24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lighting (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Fan (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Food Refrigerator (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Hot Water (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Cooling (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

HOUSEHOLD APPLIANCE

|  | Number | Power (Watt) | Total Daily use(h) | Hour of use | Remark |
| --- | --- | --- | --- | --- | --- |
| Radio/Television |  |  |  |  |  |
| Computer |  |  |  |  |  |
| Domestic refrigerator |  |  |  |  |  |
| Freezer |  |  |  |  |  |
| Ceiling fan |  |  |  |  |  |
| Washing machine |  |  |  |  |  |
| Maquinarias Marca Monafasiros | 2 | No tienen | 5 dias(35h) | 7 horas |  |
| Electrical DHW | 0 | 0 | 0 | 0 | 0 |
| Other (cafeteras, sambuchera) | 0 | 0 | 0 | 0 | 0 |
| Kitchen : Cooking set Oven | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 |
| AC system 1) Split system 2) HVAC | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 |