# INPUTS CHECKLIST COMMERCIAL

# fabrica de hielo

# tarifa INDUSTRIAL 1709 n# medidor 409239 (Foto 786,787)

La fábrica de hielo se encuentra en la Av. 12 de febrero,  la fachada principal se encuentra orientada al Oeste con pocas edificaciones a su lado, la altura con respecto a las otras edificaciones es Shorter, tiene forma cuadrada.

En la fachada uno antes de  ingresar podemos encontrar una puerta de aluminio (foto 757), al ingresar podemos observar la sala de proceso como la denominan  con 90 metros cuadrados y piso de baldosa( foto 783) ,  toda la infrestuctura del lugar es de planchas térmicas (foto 761, 762) tanto sus paredes como techos, encontramos 12 lámparas con 17 tubos floresentes en total y su utilización es máximo veinte minutos en la tarde por día (foto 761, 762, 763), podemos encontrar dos cuartos de mantenimiento con 19 metros cuadrados cada uno con planchas térmicas en su interior. (Foto 727, 728, 729) aquí dentro vemos que es totalmente cerrado y en la parte de arriba encontramos ventiladores, En este momento no se utilizan estas cámaras de mantenimiento.

Subiendo unas pequeñas gradas de baldosa podemos observar un corredor 30 metros cuadrados

(Foto 782) donde observamos las otras 2 cámaras  de congelamiento donde solo se utiliza una ahora (foto 765, 766), luego al final del corredor vemos 3cámaras de hielo de la cual solo se utiliza dos.

(Foto 771, 772, 773) la medidas de las cámaras que se encuentran arriba es de 33 metros cuadrados cada uno de ellas.

En el filo del corredor podemos observar el tanque de precio con la bomba que es utilizada para la cámara de hielo ( foto 770).

En la fachada dos podemos encontrar  motores ( foto 731, 732,733 ) de los cuales solo dos se utilizan aquí no podía observar cuantos Kw utilizan, ya que sus detalles están borrados, solo conseguí su marca ( Foto 730). Luego observamos los ventiladores ( foto 737,738,741).podemos observar ahí mismo sus conexiones de alambres ( foto 734,735,736, 756), están colocadas con barras de hierro que sostienen el alambre y  amarradas.

Luego encontramos una puerta donde  observamos la caja de breaks ( Foto 753,754,755) de las maquinas  subimos por una escalera de hierro a las maquinas de la cámara de hielo son 3 motores pero solo dos se utilizan, el techo es de ternil ( foto 751), y el piso de madera donde encontramos unas barras de hierro que sostienen los motores( foto 749)  y unos como tubos por donde baja el hielo ( foto 745), y luego podemos observar los motores ubicados una atrás de otro y todos son de la misma clase ( foto 743, 744, 746, 747), a mano derecha podemos observar el techo que cubre en la planta baja y encontrar a mano izquierda al fondo la bomba de agua marca Pedrollo consume 1550 Kw. (Foto 748).

En la facha tres no hay nada solo se ve el bloque y hierva a su lado ( Foto 760), en la fachada cuatro esta ubicada en la Av. 12 de febrero la cual es muy transitada, hay dos puertas de hierro el la una a mano derecha es la oficina donde podemos ver una radio HF, VHF,  solo se utiliza 10 minutos al día, hay una ventana de vidrio transparente de 1. 4 metros cuadrados, y el piso es de baldosa, también se puede ingresar por la sala de proceso ( foto 776, 778), y a mano izquierda encontramos otra puerta donde esta ubicada la cocina tiene 1 foco ahorrador( Foto 779), una ventana transparente de 1.4 metros cuadros ( foto 780), y una entrada de Luz ( foto 781).

Entre los techos de ternil que tiene la edificación tiene en la mitad un espacio donde entra luz y ventilación. Y se podría poner los paneles solares ( foto 784, 785)

NOTA

- Esta fabrica esta embargada por el Banco Central del Ecuador, en este momento alquila el Sr. Ramírez Segundo.

- Aquí solo trabajan 6 meses al año en época de pesca sea de pescado o langosta.

# A. Building configuration

| Construction year | 1985 |
| --- | --- |
| Orientation of main entrance | Oeste |

Density of nearby obstructions

| ( Very dense | ( Moderately dense | X Few buildings | ( Free standing |
| --- | --- | --- | --- |

Height of surrounding buildings:

| ( Higher | ( Same | X Shorter | ( Variable |
| --- | --- | --- | --- |

Building’s Shape:

| X Square | ( Rectangular | ( Square with Atrium |
| --- | --- | --- |

External Walls colour 		( dark		( medium	X light

Roof colour 			( dark		X medium	( light

| Yearly Energy consumption 01 DEL 2002 AL 07 DEL 2003 |
| --- |
| Electricity (kWh) Annual bill: | 75622 KW $ 13893.36 |

Annual operation:	from month  1    to month   6  month off       6.

Heating period:		from month      to month         .

Cooling period:		from month      to month      .

# B. Description of envelope construction

# B1.    Facade

Attention: All shading percentages below are related to total window area.

|  | Facade 1 | Facade 2 | Facade 3 | Facade 4 |
| --- | --- | --- | --- | --- |
| Facade orientation | Oeste | Norte | Este | Sur |
| Facade Area (m²) | 199 | 61 | 199 | 61 |
| Walls U-value [W/(m²K)] | Bloque | de | ceme- | nto |
| Windows area, % of facade area | 0 | 0 | 0 | 0 |
| Percentage of natural shading (%) | 0 | 0 | 0 | 0 |
| Percentage of external vertical blinds (%) | 0 | 0 | 0 | 0 |
| Percentage of external louvers (%) | 0 | 0 | 0 | 0 |
| Percentage of overhangs (%) | 0 | 0 | 0 | 0 |
| Percentage of awnings (%) | 0 | 0 | 0 | 0 |
| Percentage of side fins (%) | 0 | 0 | 0 | 0 |
| Percentage of shutters (%) | 0 | 0 | 0 | 0 |
| Percentage of internal vertical blinds (%) | 0 | 0 | 0 | 0 |
| Percentage of internal louvers (%) | 0 | 0 | 0 | 0 |

# B2.    Floor

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Floor area on the ground | 430 | Cemento con baldosa |
| Floor over non-heated zone |  |  |
| Floor exposed to the exterior (pilotis) |  |  |

# B3.    Roof

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Exposed roof area | 430 | Planchas de ternil |
| Roof area to non heated spaces | 0 | 0 |
| Roof glazed area | 0 | 0 |

#### C.    General inputs

| Parameter | Value | Description |
| --- | --- | --- |
| Site area, m² | 430 | Total lot area |
| Area of foundations, m² | 430 | Area of typical floor |
| Green Areas, m² | 0 | Green Areas |
| Height of typical floor, m | 4/ 7 | Height of typical floor |
| Number of floors | 1 | Number of floors, ground floor included. |
| Number of basement floors | 0 | Number of floors, below ground floor. |
| Number of rooms | 2 | Number of rooms |
| Number of staircases | 1 | Number of internal staircases |
| Gross floor area, m² | 430 | Gross floor area (basement included) |
| Garage area, m² | 0 | Garage area in basement |
| Heated floor area, m² | 0 | Heated floor area |
| Conditioned area, m² | 0 | Conditioned area |
| Supply air flow rate in rooms, m3/h | 0 | Supply air flow in rooms |
| Installed heating power, kW (Thermal) | 0 | Installed heating power |
| Installed cooling power (thermal), kW | 0 0 | Installed cooling power (thermal) |
| Installed electrical cooling power | 0 |  |

#### D.   Inputs for heating / cooling

| Heating set point, °C | 0 | The internal temperature is the set point temperature during the heating season. |
| --- | --- | --- |
| Cooling set point, °C | 0 | The internal temperature is the set point temperature during the cooling season. |
| Temperature control | 0 | 1: Bad control (No thermostatic control and no night set back, regulary overheating during winter) 2. No control (No thermostatic control and no night set back) 3. Standard (Thermostatic control of the indoor temperature during the heating season OR night set back of 3 °C) 4. Good control (Thermostatic control AND night setback of up to 3 °C during the heating season) 5. Advanced control (Probabilistic control of the heating system based on an estimated weather forecasts and adapted user behaviour) |
| Infiltration, ach | 0 | 1. 0.1ach 2. 0.5 ach 3. 1 ach 4. 1.5 ach |
| Boiler efficiency, % | 0 | 1. Low efficiency (Boiler in poor stage. Insulation of boiler and storage is missing. Boiler room and pipes in the boiler room are not insulated) 2. Under medium efficiency (Boiler is more than 15 years old or in a poor condition of maintenance. Insulation level of boiler and storage is insufficient) 3. Medium (Boiler is less than 15 years old OR in perfect condition. Insulation level of boiler and storage is sufficient.) 4. Over medium efficiency (Boiler is less than 15 years old and in perfect condition. Insulation level of boiler and storage is sufficient.) |
| Number of existing ceiling fans | 0 | Number of existing ceiling fans |

#### E.  Inputs for hot water production

| Fuel for domestic hot water production | 0 | 1: oil, 2:gas, 3: electricity |
| --- | --- | --- |
| Solar collectors surface, m2 |  |  |
| Available space for additional solar collectors, m2 | 430 | El techo es de planchas de ternil, y se podria poner en los lados verticales los paneles |

Available space towards south, for solar collectors:

| ( | X en los dos lados | ( |  |
| --- | --- | --- | --- |

#### Inputs for artificial lighting

|  | Internal type | External type | Power (Watt) | Daily use (h) | Remark |
| --- | --- | --- | --- | --- | --- |
| Type of existing lamps 1: standard incandescent, 2: efficient incandescent, 3: tube fluorescent, 4: compact fluorescent, 5: discharge, 6:other: Foco Ahorrador | Tipo/N#/KW 1/1/60 3/17/40 6/1/3 |  | 60w 40 3w | 1 h 0:20 min. No usan | De vez en cuando |

#### Inputs for electric CONSUMPTION

LOCALITY : Av. 12 de febrero

N. OF PERSON: 1 persona

| Contract typology: Residential Commercial Industrial Other | Type of fee:$ 1035.14 |
| --- | --- |
| Power (kW) Voltage (V):110- 240 Frequency (Hz): 60 Safety equipments: | Consumption (kWh/year) 61059 kw |

| Person | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21/22 | 22/23 | 23/24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Horas de trabajo |  |  |  | XX | XX | XX | XX |  | XX | XX | XX | XX |  |  |  |  |  |  |  |

| Plants-Equipments hours | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21-22 | 22-23 | 23-24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lighting (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 20 MIN | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Fan (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Food Refrigerator (W) |  | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX |
| Hot Water (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Cooling (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |

HOUSEHOLD APPLIANCE

|  | Number | Power (Watt) | Total Daily use(h) | Hour of use | Remark |
| --- | --- | --- | --- | --- | --- |
| Radio HF/VHF Television | 1 |  | Lunes a Viernes | 10 min |  |
| Computer |  |  |  |  |  |
| Camaras congelamiento | 2 |  | Lunes a Domingo | 24 h | Solo uno se utiliza |
| Camara de hielo | 1 |  | Lunes a Domingo | 10 a 12 h |  |
| Camaras de conservacion | 2 |  |  |  | No usan |
| Washing machine | 0 | 0 | 0 | 0 | 0 |
| Electrical space heating | 0 | 0 | 0 | 0 | 0 |
| Electrical DHW | 0 | 0 | 0 | 0 | 0 |
| Other (cafeteras, sambuchera) | 0 | 0 | 0 | 0 | 0 |
| Kitchen : Cooking set Oven | 1 0 0 | 0 0 0 | 0 0 0 | 0 0 0 | No usan 0 0 |
| AC system 1) Split system 2) HVAC | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 |