# INPUTS CHECKLIST

# Colegio ignacio hernandez

# tarifa oficial codigo 737 n# medidor 512547

# (Foto 061, 062 )

El Colegio Ignacio Hernández se encuentra ubicado en la Avenida Roldós Aguilera, esta orientada al oeste , no es una calle muy transitada por autos, podemos encontrar pocas edificaciones a su lado, la altura con las otras edificaciones que le rodean son similar, Las aulas tienen forma rectangular sus paredes de afuera son claras igual que sus techos, a la entrada del colegio ( foto 104,085) encontramos la Oficina del Director, la secretaria, y el departamento de innovación, en otro Bloque la inspección y Colecturia( foto 103) aquí se observa que el techo es de eternil, ventanas transparentes con cortinas obscuras, piso de cemento, paredes de Bloque con cemento, la temperatura que encontramos en toda esta área es de piso 24°c, las paredes 25°c, ventanas 26°c ( foto049, 054,055,052,053, 067,068,241,242).

Hay 12 aulas cada una mide 54 metros cuadrados con una altura de 3.80 metros cuadrados, con 8 lámparas y cada una tiene 2 tubos floresentes de 40 W; a lado izquierdo de las aulas podemos encontrar 12 vidrios transparentes y a lado derecho 14 vidrios, el techo es de eternil, paredes de Bloque con cemento el piso de cemento, la temperatura de las aulas es el techo 31°c, paredes 26°c, vidrios lado izquierdo 28°c, y lado derecho 26°c.( Foto 086,088,090,091,066,065,079,080).

Dentro de las 12 aulas 3 pertenecen a la área de computación, en la primera observamos 6 computadoras, donde son utilizadas por todo el colegio, en diferentes horas a la semana,(Foto 058,059,060) y usan 8 horas diarias, en el Laboratorio de computación encontramos 9 computadoras de la misma marca, con un scanner, una impresora láser, 1 switch modelo 300x, y un aire acondicionado, en este momento no es utilizado este laboratorio hasta que oficialmente sea entregado por las personas que donaron los equipos( foto 243,244,245,246,247,248).

Luego vamos a otras de las aulas que se les denomina Laboratorio de ingles donde los estudiantes pueden escuchar, y tener mas practica.( foto 092,093,094,095,096).

El colegio tiene 3 hectárea, de las cuales solo 5000 metros cuadrados son utilizados aquí podemos encontrar sus aulas, oficinas administrativas una cancha de básquet y fotboll(Foto 075,098,099,100,101,102,097,069,108) y lo otro es lleno de piedra y pocos árboles.

En el Colegio encontramos un bar, donde tiene una refrigeradora que se encuentra prendida las 24 horas, y un foco de 100 w, pero tiene su propio medidor, el techo es de pernil y madera, el piso de cemento.( 056, 057)

La bomba de Agua( foto 050, 051) tiene su tanque de presión, con 989 w, es automática y se prende tres veces al día, un promedio de una Hora por día

Nota

- Las medidas de las fachadas fueron tomadas de las aulas, cada una tiene la misma característica en mediciones y estructura.

- Aquí hay 150 alumnos y 20 profesores.

- Es una área muy grande donde se podría dar la opción de poner paneles solares.

- El medidor que tienen es utilizada para todas las aulas y la oficina de administración.

- La oficina de inspección y colectaría tiene su propio medidor.

- Áreas verdes como árboles hay muy poco, pero existe el espacio suficiente para poder sembrar y ayudar que las aulas sean protegida de sombra natural, ya que el calor que el techo eternil produce al medio día es de 40°c dentro de las aulas.

- Las conecciones de electricas no son muy buenas ( foto 097)

- El colegio solo utiliza las luces cuando hay fiestas y esto es tres veces al año, por una hora,

Lo que mas consumen son las computadoras, radios, foto copiadora y bomba de agua.

# A. Building configuration

| Construction year | 1996 |
| --- | --- |
| Orientation of main entrance | Oeste |

Density of nearby obstructions

| ( Very dense | ( Moderately dense | X Few buildings | ( Free standing |
| --- | --- | --- | --- |

Height of surrounding buildings:

| ( Higher | X Same | ( Shorter | ( Variable |
| --- | --- | --- | --- |

Building’s Shape:

| ( Square | X Rectangular | ( Square with Atrium |
| --- | --- | --- |

Nota: todas las aulas tienen forma rectangular

External Walls colour 		( dark		( medium	X light

Roof colour 			( dark		( medium	X light

| Yearly Energy consumption 01 DEL 2002 AL 07 DEL 2003 |
| --- |
| Electricity (kWh) Annual bill: | 3092 KW $273.40 |

Annual operation:	from month   Abril   to month  Enero   month off   Febrero, Marzo, Abril .

Heating period:		from month      to month         .

Cooling period:		from month      to month      .

# B. Description of envelope construction

# B1.    Facade

Attention: All shading percentages below are related to total window area.

|  | Facade 1 | Facade 2 | Facade 3 | Facade 4 |
| --- | --- | --- | --- | --- |
| Facade orientation | Oeste | Norte | Este | Sur |
| Facade Area (m²) de las aulas | 34 | 23 | 34 | 23 |
| Walls U-value [W/(m²K)] | Bloque | con | cemen | to |
| Windows area, % of facade area | 50% | 0 | 50% | 0 |
| Percentage of natural shading (%) | 0 | 0 | 0 | 0 |
| Percentage of external vertical blinds (%) | 50% | 0 | 50% | 0 |
| Percentage of external louvers (%) | 0 | 0 | 0 | 0 |
| Percentage of overhangs (%) | 0 | 0 | 0 | 0 |
| Percentage of awnings (%) | 0 | 0 | 0 | 0 |
| Percentage of side fins (%) | 0 | 0 | 0 | 0 |
| Percentage of shutters (%) | 0 | 0 | 0 | 0 |
| Percentage of internal vertical blinds (%) | 50% | 0 | 50% | 0 |
| Percentage of internal cortinas (%) | 5% | 0 | 5% | 0 |

Nota: Los % de ventanas es un estimado que se dio.

# B2.    Floor de las Aulas

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Floor area on the ground | 54 | Cemento |
| Floor over non-heated zone | 0 | 0 |
| Floor exposed to the exterior (pilotis) | 0 | 0 |

# B3.    Roof de las Aulas

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Exposed roof area | 55 | Techo de eternil |
| Roof area to non heated spaces | 0 | 0 |
| Roof glazed area | 0 | 0 |

#### C.    General inputs

| Parameter | Value | Description |
| --- | --- | --- |
| Site area, m² Area total del Colegio | 3 hectares | Total lot area |
| Area of foundations, m² Area de construccion | 5.000 m² | Area of typical floor |
| Green Areas, m² | 0 | Green Areas |
| Height of typical floor, m | 3.80 m | Height of typical floor |
| Number of floors | 1 | Number of floors, ground floor included. |
| Number of basement floors | 0 | Number of floors, below ground floor. |
| Number of rooms Numero total aulas y oficinas | 16 | Number of rooms |
| Number of staircases | 0 | Number of internal staircases |
| Gross floor area, m² | 3 hectares | Gross floor area (basement included) |
| Garage area, m² | 0 | Garage area in basement |
| Heated floor area, m² | 0 | Heated floor area |
| Conditioned area, m² | 0 | Conditioned area |
| Supply air flow rate in rooms, m3/h | 0 | Supply air flow in rooms |
| Installed heating power, kW (Thermal) | 0 | Installed heating power |
| Installed cooling power (thermal), kW |  | Installed cooling power (thermal) |
| Installed electrical cooling power | 2 | Aula de computacion |

#### D.   Inputs for heating / cooling

| Heating set point, °C | 0 | The internal temperature is the set point temperature during the heating season. |
| --- | --- | --- |
| Cooling set point, °C | 0 | The internal temperature is the set point temperature during the cooling season. |
| Temperature control | 0 | 1: Bad control (No thermostatic control and no night set back, regulary overheating during winter) 2. No control (No thermostatic control and no night set back) 3. Standard (Thermostatic control of the indoor temperature during the heating season OR night set back of 3 °C) 4. Good control (Thermostatic control AND night setback of up to 3 °C during the heating season) 5. Advanced control (Probabilistic control of the heating system based on an estimated weather forecasts and adapted user behaviour) |
| Infiltration, ach | 0 | 1. 0.1ach 2. 0.5 ach 3. 1 ach 4. 1.5 ach |
| Boiler efficiency, % | 1 | 1. Low efficiency (Boiler in poor stage. Insulation of boiler and storage is missing. Boiler room and pipes in the boiler room are not insulated) 2. Under medium efficiency (Boiler is more than 15 years old or in a poor condition of maintenance. Insulation level of boiler and storage is insufficient) 3. Medium (Boiler is less than 15 years old OR in perfect condition. Insulation level of boiler and storage is sufficient.) 4. Over medium efficiency (Boiler is less than 15 years old and in perfect condition. Insulation level of boiler and storage is sufficient.) |
| Number of existing ceiling fans | 0 | Number of existing ceiling fans |

#### E.  Inputs for hot water production

| Fuel for domestic hot water production |  | 1: oil, 2:gas, 3: electricity |
| --- | --- | --- |
| Solar collectors surface, m2 |  |  |
| Available space for additional solar collectors, m2 | 55 m2 | Laboratorio de computación , el techo es de eternil |

Available space towards south, for solar collectors:

| X | ( | ( |  |
| --- | --- | --- | --- |

#### Inputs for artificial lighting

|  | Internal type | External type | Power (Watt) | Daily use (h) | Remark |
| --- | --- | --- | --- | --- | --- |
| Type of existing lamps 1: standard incandescent, 2: efficient incandescent, 3: tube fluorescent, 4: compact fluorescent, 5: discharge, 6:other | 7 192 | 15 | 100w 40w | 1h |  |

Nota : solo se usa los focos 100w, 1 h, en la oficina del director;y usan todas las luces solo cuando hay fiestas que es tres veces al año y solo una hora

#### Inputs for electric CONSUMPTION

LOCALITY :Av. Roldos Aguilera

N. OF PERSON: 20 Personas contando con los profesores y administración

| Contract typology: Residential Commercial Industrial Other Colegio Ignacio Hernandez | Type of fee: $20.05 |
| --- | --- |
| Power (kW) Voltage (V): 110-220 Frequency (Hz): 60 Safety equipments: | Consumption (kWh/year) 1813 kw |

| Person | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21/22 | 22/23 | 23/24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Horas De Trabajo |  |  | XX | XX | XX | XX | XX | XX | X | X | XX | X |  |  |  |  |  |  |  |

Nota: Solo la parte administrativa trabaja en la tarde de 2:15 pm, a 4:15, y en la mañana es la entrada de los profesores y administración

| Plants-Equipments hours | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21-22 | 22-23 | 23-24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lighting (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | X | 0 | 0 | 0 | 0 | 0 | 0 |
| Fan (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Food Refrigerator (W) | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX | XX |
| Hot Water (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Cooling (W) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

Nota: Las luces usan solo en fiestas que el colegio da, que son 3 veces al año, y utilizan una hora

HOUSEHOLD APPLIANCE

|  | Number | Power (Watt) | Total Daily use(h) | Hour of use | Remark |
| --- | --- | --- | --- | --- | --- |
| Radio Television VH Ventilador Fotocopiadora | 4 2 1 1 1 | W 50 w 18W 65 W 1350 W | Lunes a Viernes Lunes a Viernes 1 vez por semana Lunes a Viernes Lunes a Viernes | 5 h 1h 1h 8 h 30min | Epoca dic-may |
| Computer Scaner | 19 1 | 150w | Lunes a Viernes | 8h |  |
| Domestic refrigerator | 1 | 560w | Lunes a Lunes | 24 h | Aqui tienen otro medidor, ya que es el área del bar |
| Freezer | 0 | 0 | 0 | 0 | 0 |
| Ceiling fan | 0 | 0 | 0 | 0 | 0 |
| Washing machine | 0 | 0 | 0 | 0 | 0 |
| Electrical space heating | 0 | 0 | 0 | 0 | 0 |
| Electrical DHW | 0 | 0 | 0 | 0 | 0 |
| Other (cafeteras, sambuchera) | 0 | 0 | 0 | 0 | 0 |
| Kitchen : Cooking set Oven | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 |
| AC system 1) Split system 2) HVAC | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 |