# INPUTS CHECKLIST

# Testigos de Jehova

# tarifa beneficio publico 984 n# medidor 622227 (Foto 341)

El templo de los Testigos de Jehová se encuentra ubicado en la Av. Alsacio Nortia, es una avenida muy transitada, la densidad  con respecto a las edificaciones Moderately dense, la altura con las edificaciones es similar, tiene forma cuadrada, sus paredes son claras, y el techo medio claro.

En La fachada uno( Foto 317)  podemos observar la entrada al templo donde tiene, un pequeño corredor de 13metros cuadrados ( foto 316) al ingresar a mano derecha encontramos la bodega de la bombas con el tanque de presión se utiliza 6 horas al mes, sus conexiones no son muy buenas, el techo es de eternil con vigas de madera( foto 310, 311, 312, 313)  al ingresar  templo observamos que tienen focos de 100w, el techo es, tumbado de yeso, el piso baldosa, las paredes de Bloque de cemento con Pilares( Foto 307, 308).

La temperatura que encontramos dentro del templo es de las paredes 22°c, techo de tumbado 22°c, piso de baldosa 23°c.

En el fondo a mano derecha encontramos un cuarto donde esta un amplificador que es utilizado solo los días de Culto son Martes Jueves y Sábados ( foto 306)

En la Fachada principal podemos ver una casa de dos pisos, solo se utiliza el piso de abajo y tiene su propio medidor (foto 314).

Nota

- El templo va hacer reconstruido el próximo año, van a cambiar las luces de ahora, por luces floresentes, las bombas van hacer cambiadas también

- El techo de arriba del templo va hacer cambiado  ya que en este momento se encuentran las vigas de madera mal.

- Aquí el mayor consumo son las ñluces que utilizan ya que son de 100 w.

- Los aires acondicionados solo son utilizados en epoca de calor desde Diciembre hasta Mayo,

# A. Building configuration

| Construction year | 1992 |
| --- | --- |
| Orientation of main entrance | Este |

Density of nearby obstructions

| ( Very dense | X Moderately dense | ( Few buildings | ( Free standing |
| --- | --- | --- | --- |

Height of surrounding buildings:

| ( Higher | X Same | ( Shorter | ( Variable |
| --- | --- | --- | --- |

Building’s Shape:

| X Square | ( Rectangular | ( Square with Atrium |
| --- | --- | --- |

External Walls colour 		( dark		( medium	X light

Roof colour 			( dark		X medium	( light

| Yearly Energy consumption 01 del 2002 al 07 del 2003 |
| --- |
| Electricity (kWh) Annual bill: | Kw 4434 $ 140.63 |

Annual operation:	from month   1   to month  12   month off       .

Heating period:		from month      to month         .

Cooling period:		from month      to month      .

# B. Description of envelope construction

# B1.    Facade

Attention: All shading percentages below are related to total window area.

|  | Facade 1 | Facade 2 | Facade 3 | Facade 4 |
| --- | --- | --- | --- | --- |
| Facade orientation | Este | Norte | Oeste | Sur |
| Facade Area (m²) | 19 | 43 | 19 | 43 |
| Walls U-value [W/(m²K)] | Bloque | de | cemen | to |
| Windows area, % of facade area | 0 | 0 | 0 | 0 |
| Percentage of natural shading (%) | 0 | 0 | 0 | 0 |
| Percentage of external vertical blinds (%) | 0 | 0 | 0 | 0 |
| Percentage of external louvers (%) | 0 | 0 | 0 | 0 |
| Percentage of overhangs (%) | 0 | 0 | 0 | 0 |
| Percentage of awnings (%) | 0 | 0 | 0 | 0 |
| Percentage of side fins (%) | 0 | 0 | 0 | 0 |
| Percentage of shutters (%) | 0 | 0 | 0 | 0 |
| Percentage of internal vertical blinds (%) | 0 | 0 | 0 | 0 |
| Percentage of internal louvers (%) | 0 | 0 | 0 | 0 |

# B2.    Floor

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Floor area on the ground | 140 m2 | Es de Cemento con baldosa |
| Floor over non-heated zone | 0 | 0 |
| Floor exposed to the exterior (pilotis) | 13 m2 | Es de Cemento con baldosa |

# B3.    Roof

|  | Area (m2) | U – value [W/(m²K)] |
| --- | --- | --- |
| Exposed roof area | 10.33 m2 | Techo de Zing metalico |
| Roof area to non heated spaces | 0 | 0 |
| Roof glazed area | 0 | 0 |

#### C.    General inputs

| Parameter | Value | Description |
| --- | --- | --- |
| Site area, m² | 150 m² | Total lot area |
| Area of foundations, m² | 140 m² | Area of typical floor |
| Green Areas, m² | 0 | Green Areas |
| Height of typical floor, m | 2.8m | Height of typical floor |
| Number of floors | 1 | Number of floors, ground floor included. |
| Number of basement floors | 0 | Number of floors, below ground floor. |
| Number of rooms | 2 | Number of rooms |
| Number of staircases | 0 | Number of internal staircases |
| Gross floor area, m² | 150 m² | Gross floor area (basement included) |
| Garage area, m² | 0 | Garage area in basement |
| Heated floor area, m² | 0 | Heated floor area |
| Conditioned area, m² | 0 | Conditioned area |
| Supply air flow rate in rooms, m3/h | 0 | Supply air flow in rooms |
| Installed heating power, kW (Thermal) |  | Installed heating power |
| Installed cooling power (thermal), kW | 0 | Installed cooling power (thermal) |
| Installed electrical cooling power | 2 |  |

#### D.   Inputs for heating / cooling

| Heating set point, °C | 0 | The internal temperature is the set point temperature during the heating season. |
| --- | --- | --- |
| Cooling set point, °C | 0 | The internal temperature is the set point temperature during the cooling season. |
| Temperature control | 0 | 1: Bad control (No thermostatic control and no night set back, regulary overheating during winter) 2. No control (No thermostatic control and no night set back) 3. Standard (Thermostatic control of the indoor temperature during the heating season OR night set back of 3 °C) 4. Good control (Thermostatic control AND night setback of up to 3 °C during the heating season) 5. Advanced control (Probabilistic control of the heating system based on an estimated weather forecasts and adapted user behaviour) |
| Infiltration, ach |  | 1. 0.1ach 2. 0.5 ach 3. 1 ach 4. 1.5 ach |
| Boiler efficiency, % | 2 | 1. Low efficiency (Boiler in poor stage. Insulation of boiler and storage is missing. Boiler room and pipes in the boiler room are not insulated) 2. Under medium efficiency (Boiler is more than 15 years old or in a poor condition of maintenance. Insulation level of boiler and storage is insufficient) 3. Medium (Boiler is less than 15 years old OR in perfect condition. Insulation level of boiler and storage is sufficient.) 4. Over medium efficiency (Boiler is less than 15 years old and in perfect condition. Insulation level of boiler and storage is sufficient.) |
| Number of existing ceiling fans | 0 | Number of existing ceiling fans |

#### E.  Inputs for hot water production

| Fuel for domestic hot water production |  | 1: oil, 2:gas, 3: electricity |
| --- | --- | --- |
| Solar collectors surface, m2 |  |  |
| Available space for additional solar collectors, m2 | 10.33 m2 | El techo esta un poco, Viejo, tiene vigas de Madera dañas, y va hacer cambiado, se podría poner en toda el área del techo |

Available space towards south, for solar collectors:

| X | ( | ( |  |
| --- | --- | --- | --- |

#### Inputs for artificial lighting

|  | Internal type | External type | Power (Watt) | Daily use (h) | Remark |
| --- | --- | --- | --- | --- | --- |
| Type of existing lamps 1: standard incandescent, 2: efficient incandescent, 3: tube fluorescent, 4: compact fluorescent, 5: discharge, 6:other | 26 0 0 0 0 0 | 4 0 0 0 0 0 | 100 W 0 0 0 0 0 | 8H 0 0 0 0 0 |  |

#### Inputs for electric CONSUMPTION

LOCALITY : Av Alsacio Nortia

N. OF PERSON: 5 personas, del templo, pero lo hacen como voluntarias

| Contract typology: Residential Commercial Industrial Other Beneficio Publico | Type of fee:$ 18.68 |
| --- | --- |
| Power (kW) Voltage (V):110 Frequency (Hz):60 Safety equipments: | Consumption (kWh/year) 2641kw |

| Person | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21/22 | 22/23 | 23/24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |

Nota: es un servicio voluntario no tienen horas de trabajo

| Plants-Equipments hours | Night | 6÷7 | 7÷8 | 8÷9 | 9÷10 | 10÷11 | 11÷12 | 12÷13 | 13÷14 | 14-15 | 15-16 | 16/17 | 17/18 | 18/19 | 19-20 | 20/21 | 21-22 | 22-23 | 23-24 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lighting (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | X | XX | XX | XX | 0 | 0 |
| Fan (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Food Refrigerator (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Hot Water (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Cooling (W) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | XX | XX | XX | XX | 0 | 0 |

Nota: El aire acondicionado solo se utiliza en época de calor a partir de Diciembre hasta Mayo

HOUSEHOLD APPLIANCE

|  | Number | Power (Watt) | Total Daily use(h) | Hour of use | Remark |
| --- | --- | --- | --- | --- | --- |
| Sistema de amplificacion | 1 | 60w | Martes, Jueves y sabado | 6h |  |
| Computer | 0 | 0 | 0 | 0 | 0 |
| Domestic refrigerator | 0 | 0 | 0 | 0 | 0 |
| Freezer | 0 | 0 | 0 | 0 | 0 |
| Ceiling fan | 0 | 0 | 0 | 0 | 0 |
| Washing machine | 0 | 0 | 0 | 0 | 0 |
| Electrical space heating | 0 | 0 | 0 | 0 | 0 |
| Electrical DHW | 0 | 0 | 0 | 0 | 0 |
| Other (cafeteras, sambuchera) | 0 | 0 | 0 | 0 | 0 |
| Kitchen : Cooking set Oven | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 |
| AC system 1) Split system 2) HVAC | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 | 0 0 0 |